## Slide 1: Transpired
Diana, Justin, David
3/3/22

## Slide 2: Overview
25 x 25 cell grid
  dx and dy = 100 m. One vertical layer with dz = 15 m
Constand head boundaries & steady state
  Left head 15 m, right head 5 m
  Water table elevation less than aquifer thickness→ unconfined aquifer
Local area of recharge at [6:10,6:10]
  Rate: 5*10-4 m / day / cell * 10,000 m2 per cell * 16 cells = 80 m3 / day recharge
ET potentially across entire domain, if water table depth (WTD) < extinction depth in that cell
  WTD = Vertical Layer Thickness (15 m) minus Head
  Rate 5*10-5 m / day / cell
Pumping well at [10,15]
  When turned on, pumps at 20 m3 / day
K = 1 m/d
Recharge
dz = 15m
Constant head boundary 15m
Constant head boundary 5m
Well

## Slide 3: Challenge 1
For the initial boundary head values (15 and 5) and recharge (5e-4) and ET rates (5e-5):
We see the left boundary flow dip about halfway between the recharge area and the bottom boundary. The high flow above the dip is the system’s response to balance spreading recharge and maintain the specified head of 15.
In the next slide, we see that the introduced recharge affects the gradient, diverting much of the inflow away from the recharge zone and down near the bottom of domain, increasing the flow of the bottom boundary.

## Slide 4: The recharge reaches much of the down-gradient domain. We can see that water from the upper left boundary is diverted from its left-to-right path and incorporates downward movement. This can help explain the higher flow rate near the bottom of the right boundary from the previous question.
Challenge 1

## Slide 5: Challenge 1
Plot ET,Recharge and Water Table depth and explain why we see the patterns we do.

## Slide 6: Challenge 2
Calculate the water balance for the model
  Report all of the inflows and outflows with units and show that mass is being balanced.
  dS/dt = output - input
  0 = Q_out + ET - Q_in - R
  Q_out + ET = Q_in + R
  116 m3/d + 70 m3/d = 106 m3/d + 80 m3/d
  186 m3/d = 186 m3/d
Inflows (input) | Outflows (output)
Flux in (Q_in) Recharge (R) | Flux out (Q_out) Evapotranspiration (ET)

## Slide 7: Challenge 2
Explain what controls each term in your water balance
Terms | Controls
Flux in (Q_in) | Boundary conditions, head gradient, K, area
Recharge (R) | Input Values, Area
Flux Out (Q_out) | Boundary conditions, head gradient, K, area
Evapotranspiration (ET) | Input Value, Extinction Depth, Area

## Slide 8: Challenge 3, part I
Changing extinction depth from 3m to 1m:
dS/dt = input - output
  0 = Qin + R - Qout - ET
  Qout + ET = Qin + R
125 m3/d + 34 m3/d = 79 m3/d + 80 m3/d
159 m3/d = 159 m3/d
Evapotranspiration removes less water from the system because its extinction depth is shallower than 3m. With lower ET and a constant recharge, less water is needed to cross the left boundary for its specified head, but more water must flow out the right boundary.

## Slide 9: Challenge 3, part II
Changing extinction depth from 3m to 8m:
dS/dt = input - output
  0 = Qin + R - Qout - ET
  Qout + ET = Qin + R
88 m3/d + 132 m3/d = 140 m3/d + 80 m3/d
220 m3/d = 220 m3/d
Evapotranspiration removes more water from the system because its extinction depth is deeper than previously. With higher ET and a constant recharge, more water is needed to cross the left boundary for its specified head, but less water must flow out the right boundary.

## Slide 10
Extinction Depth 1
(No pumping)
Extinction Depth 3
(No pumping)
Extinction Depth 8
(No pumping)

## Slide 11: Challenge 4
Well begins pumping: extracting 20 m3/day.
How does the well change the zone that is affected by the recharge area
How does it affect the ET map?
See next slides for further discussion

## Slide 12
No Pumping
Extinc. Depth 1
Extinc. Depth 3
Extinc. Depth 8
Pumping
Notes: Explain why we see the ET, RCH, and WTD patterns.
How does the well change the zone that is affected by the rch area?
It minimizes its impact. You can see in each scenario comparison, the WTD bulge that benefits from recharge is narrowed once well pumping begins.
How does it affect the ET map?
It reduces the amount of ET that occurs in all scenarios but with to a higher degree in ET maps that represent deeper extinction depths.

## Slide 13: Challenge 5
Inflows (input) | Outflows (output)
[10,14] Flux Right Face [10,15] Flux Right Face [9,15] Flux Front Face [10,15] Flux Front Face | Well Pumping (W) ET? No, because depth to WT > extinction depth
Write a mass balance for the well:
dS/dt = input - output
  0 = Qin - W
  Qin = W
10.03 m3/d + .08 m3/d + 5.41 m3/d + 4.49 m3/d = 20 m3/d
20 m3/d = 20 m3/d

## Slide 14
K = 1 m/d
10.03
0.08
4.49
5.41
Python Coordinates
Head
Flux (m3 / day)
Qout = - 20

## Slide 15
FFF
FRF
FRF
FFF
[9,15]
[10,14]
[10,15]
This diagram shows the cells that flux for the well is calculated at.
Note: there are only 3 cells that determine our flux at the well!
The FFF of the cell above ([9,15]) the well
The FFF of the well cell ([10,15])
The FRF of the cell to the left ([10,14]) of the cell
The FRF of the well cell ([10,15])

## Slide 16: Challenge 5
How much water captured by the well is coming from a boundary?
  Based off flow lines, almost none
How much is originating as recharge?
  Based off flow lines, almost all of it
  80 m3 / day of recharge, well captures ~20 m3 / day of it
How do you account for ET?
  ET at and around well is zero for extinction depth of 3m, because WTD in that area is ~5-6 m.
At steady state, what are the effects of 'capture' by the well?
  For entire domain, total ET reduced from 70.35 m3 / day to 66.27 m3 / day
  Flow leaving right boundary is less than flow entering left boundary (opposite is true if well is turned off).
No Pumping
Pumping

## Slide 17: Questions?